## Slide 1: Efficacy of Improved Hydrogen Peroxide Against Important Healthcare-Associated Pathogens
William A. Rutala, Ph.D., M.P.H.1,2, Maria F. Gergen, M.T. (ASCP),1
David J. Weber, M.D., M.P.H.1,2
1Hospital Epidemiology
University of North Carolina Health Care
Chapel Hill, NC 27514
2Division of Infectious Diseases
University of North Carolina School of Medicine
Chapel Hill, NC 27599-7030

## Slide 2
Key words:
Hydrogen peroxide, surface disinfection, environment
Running Head:
Improved Hydrogen Peroxide
Word Count:
1198
Acknowledgement:
We acknowledge Dr. Emily Sickbert-Bennett for the statistical analysis.
Potential Conflicts of Interest:
Drs. Rutala and Weber have been a consultant to Clorox and Advanced Sterilization Products within the past three years.

## Slide 3: ABSTRACT
This study was designed to test in vitro efficacy of two improved hydrogen peroxide (HP) products against three standard HP products and one QUAT. Improved HP is significantly superior to standard HP at the same concentration and can be used for disinfection of environmental surfaces or noncritical patient care items.

## Slide 4: Introduction
An improved hydrogen peroxide-based technology has been introduced into health care for disinfection of noncritical environmental surfaces and patient equipment1 and high-level disinfection of semicritical equipment such as endoscopes.2-4 Improved hydrogen peroxide (HP) contains very low levels of anionic and/or nonionic surfactants in an acidic product which act with HP to produce microbicidal activity. This combination of ingredients speeds the antimicrobial activity of hydrogen peroxide and cleaning efficiency.3, 4

## Slide 5: Introduction - continued
Improved HP is considered safe for humans and equipment, and benign for the environment. In fact, improved HP has the lowest EPA toxicity category (i.e.,category IV) based on its oral, inhalation and dermal toxicity which means it is practically non-toxic and not an irritant.1, 3, 5 It is prepared and marketed by several companies in various concentrations (e.g., 0.5%-7%) and different products may use different terminology for these products such as “accelerated” or “activated”. Lower concentrations (i.e., 0.5%,1.4%) are designed for the low-level disinfection of noncritical environmental surfaces and patient care objects while the higher concentrations (i.e., >2%) can be used as high-level disinfectants for semicritical medical devices (e.g., endoscopes).

## Slide 6: Introduction - continued
The purpose of the study was to evaluate the antimicrobial activity of new HP formulations designed for disinfection on noncritical environmental surfaces and noncritical patient care equipment with older standard HP formulations and a quaternary ammonium compound (QUAT).

## Slide 7: Methods – Disinfectants Tested
We tested the following disinfectants: A456-II a QUAT (Ecolab, St. Paul, MN) at 1:256; Clorox Healthcare™ Hydrogen Peroxide Cleaner Disinfectant (Clorox Company, Oakland, CA), undiluted; hydrogen peroxide (Owens and Minor, Mechanicsville, VA) at undiluted (3.0%), 1.4% and 0.5%; and OxivirTB (Johnson Diversey, Inc., Sturtevant, WI), undiluted.

## Slide 8: Methods – Test Organisms
We tested three epidemiologically-important pathogens: a community-acquired methicillin-resistant Staphylococcus aureus strain (USA300); vancomycin-resistant Enterococcus (ATCC# 51299); and multidrug-resistant (MDR) Acinetobacter baumannii (clinical strain).

## Slide 9: Methods – Test Organisms - continued
Our test organism suspensions were prepared fresh daily by plating each organism to sheep blood agar (SBA)(Remel, Lenexa, KS) and incubating it at 37oC for ~18 hours before each run. Immediately before each run, 0.5 McFarland standard suspensions were prepared from these plates, separately, for each organism in Trypticase Soy Broth (TSB)(Remel, Lenexa, KS). To simulate loading with organic material, fetal calf serum (Remel, Lenexa, KS) at a final concentration of 5% was added to the TSB.

## Slide 10: Methods – Disinfectant Testing
The second tier of a quantitative carrier test, a standard of ASTM International, was used to determine the bactericidal activity of the formulations.6 In this test, stainless steel disks (1 cm diameter x 0.7 mm thick; Muzeen and Blythe, Winnipeg, MB) were contaminated with 10µl of test suspension (103-106 CFU of the test organism). To detect low-level antimicrobial activity (i.e., < 3 log10 reduction), a lower inoculum (103 CFU/carrier) was used when the disinfectant showed no bactericidal activity at the higher microbial load. One disk each was placed, with contaminated side up, at the bottom of a sterile 20ml glass vial, covered with 50µl of the test disinfectant and held for the desired contact time (e.g., 30 seconds, 1 minute) at room temperature (20o±2oC).

## Slide 11: Methods – Disinfectant Testing - continued
We did not test times greater than 1 minute which may have been part of the label claim (e.g., 10 minutes) because these longer times are difficult to achieve in practice. At the end of the contact time, the action of the disinfectant was stopped by the addition of 9.95ml neutralizer (0.85% NaCl + 0.1% Tween 80% + 3% glycine [except for quaternary ammonium compound used 1% sodium thiosulfate] at pH=7.2–7.4). The contents of the vial were vortexed on high for 1 minute to elute the inoculum from the surface of the disks. The eluates and three washes of the vials with sterile saline were passed through a membrane filter (Savur analytical funnel containing a 0.22µ filter; GE Water and Process Technologies, Trevose, PA). After the vial had been adequately rinsed, the sides of the analytical funnel were rinsed with 40ml of sterile saline. Each filter was aseptically placed on the surface of SBA and incubated at 37oC for 48 hours. After 48 hours, the CFU were counted and the log10 reductions were calculated.

## Slide 12: Results
The bactericidal activities of the disinfectants tested are displayed in Table 1 and the statistical analysis is summarized in Table 2. The two improved HP products had similar effectiveness (e.g., >6 log10 reduction within 30 seconds) against the test organisms and were significantly superior to all three concentrations of HP. The improved HP products were superior or similar to the QUAT tested. The standard HP products (i.e., 3.0%, 1.4%, 0.5%) generally had similar bactericidal activity. Finally, the QUAT was significantly superior or similar to the standard HP products. These relationships held true regardless of the presence or absence of fetal calf serum and contact time.

## Slide 13: Discussion
There is excellent evidence in the scientific literature that environmental contamination plays an important role in the transmission of MRSA, VRE, C. difficile and Acinetobacter.7, 8 These pathogens have been demonstrated to persist in the environment for days (and in some cases months), to frequently contaminate the environmental surfaces in rooms of colonized or infected patients, to transiently colonize the hands of healthcare personnel, to be transmitted by healthcare personnel, and to cause outbreaks in which environmental transmission was deemed to play a role. Furthermore, admission to a room in which the previous patient had been colonized or infected with MRSA, VRE, C. difficile or Acinetobacter has been shown to be a risk factor for the newly admitted patient to develop colonization or infection.7, 8 Although environmental contamination has been demonstrated as an important component of patient-to-patient transmission of these pathogens, the effectiveness of disinfectants to clean contaminated surfaces has not been completely assessed.

## Slide 14: Discussion - continued
It has long been recommended in the United States that environmental surfaces in patient rooms be cleaned and disinfected on a regular basis (e.g.,daily,3x per week), when surfaces are visibly soiled, and after patient discharge.9 Disinfection is generally performed using a one-step process with and an EPA-registered hospital disinfectant such as a QUAT. We compared the bactericidal activity of a QUAT to two new improved HP products. The improved HP appeared to be superior or similar to the QUAT tested. When the two improved HP products were compared to 0.5%, 1.4% and 3% HP formulations, the improved HP-based environmental surface disinfectants proved to be more effective (>6-log10 reduction) and fast-acting (30-60 seconds) microbicides in the presence of a soil load (to simulate the presence of body fluids) than commercially-available HP. Only 30-60 second contact time was studied because longer contact times (e.g., 10 minutes) are not achievable in clinical practice. It appears, therefore, that the surfactants were able to significantly increase the bactericidal activity of HP. Additionally, the improved HP products have an EPA-registered contact time that is substantially less than most EPA-registered low-level disinfectants.

## Slide 15: Discussion - continued
Standard HP is among the oldest microbicides; however, it is relatively unstable, somewhat slow acting, and has limited antimicrobial activity. The stabilizers, surfactants and other excipients added to the improved HP formulations have addressed these weaknesses.1 Improved HP was also more effective than the tested quaternary ammonium compound and standard HP. Thus, improved HP offers an option for non-critical environmental surfaces and patient equipment and it addresses some concerns associated with some low-level disinfectants (e.g., toxicity, a contact time of 30-60 seconds).

## Slide 16
Table 1. Bactericidal activity of disinfectants (log10 reduction) with a contact time of 30 seconds or 1 minute at 20oC with and without fetal calf serum (FCS)1
Organism |  | OxivirTB (0.5% H2O2) | 0.5% H2O2 | CHHPCD (1.4% H2O2) | 1.4% H2O2 | 3.0% H2O2 | A456-II (QUAT) | 
~106 Inoculum - Contact Time = 1 minute – No 5% FCS |  |  |  |  |  |  |  | 
MRSA | >6.62 |  | <4.04 | >6.54 | <4.04 | <4.04 |  | 5.55
VRE | >6.34 |  | <3.61 | >6.13 | <3.61 | <3.61 |  | 4.58
MDR A.baumannii | >6.76 |  | <4.28 | >6.76 | <4.28 | <4.28 |  | >6.76
~106 Inoculum - Contact Time = 30 seconds – No 5% FCS |  |  |  |  |  |  |  | 
MRSA | >6.64 |  | NT | >6.64 | NT | <4.16 |  | <4.16
VRE | >6.28 |  | NT | >6.28 | NT | <3.80 |  | <3.80
MDR A. baumannii | >6.76 |  | NT | >6.76 | NT | <4.28 |  | 6.11
~103 Inoculum - Contact Time = 1 minute – No 5% FCS |  |  |  |  |  |  |  | 
MRSA | >3.71 |  | <1.23 | >3.71 | <1.23 | <1.23 |  | >3.71
VRE | >3.26 |  | 1.45 | >3.26 | NT | 1.40 |  | >3.26
MDR A. baumannii | >3.53 |  | <1.05 | >3.53 | 1.75 | >3.53 |  | >3.53
~106 Inoculum - Contact Time = 1 minute – 5% FCS Present |  |  |  |  |  |  |  | 
MRSA | >6.72 |  | NT | >6.72 | NT | <4.24 |  | <4.24
VRE | >6.26 |  | NT | >6.26 | NT | <3.78 |  | <3.78
MDR A. baumannii | >6.56 |  | NT | >6.56 | NT | <4.08 |  | >6.56
MDR, multi-drug-resistant; MRSA, methicillin-resistant Staphylococcus aureus; VRE, vancomycin-resistant Enterococcus ; NT, not tested; FCS, fetal calf serum; CHHPCD, Clorox Healthcare™ Hydrogen Peroxide Cleaner Disinfectant
1Individual mean values may have the same result because the same inoculums on the same day may have been run against multiple disinfectants. If complete killing occurred the minimum inactivation would equal the initial inoculum. Some results reported as “greater than X” because complete killing of the inoculums occurred.

## Slide 17: Table 2. Comparative efficacy of improved hydrogen peroxide, standard hydrogen peroxide and a quaternary ammonium compound*
 | OxivirTB | 0.5% HP | CHHPCD | 1.4% HP | 3.0% HP | A456-II
OxivirTB | --- | OxivirTB > 0.5% HP | OxivirTB = CHHPCD | OxivirTB> 1.4% HP | OxivirTB> 3.0% HP** | OxivirTB > or = A456-II
0.5% HP | OxivirTB > 0.5% HP | --- | CHHPCD > 0.5% HP | 1.4% HP > or = 0.5% HP | 3.0% HP > or = 0.5% HP | A456-II > or = 0.5% HP
CHHPCD | OxivirTB = CHHPCD | CHHPCD > 0.5% HP | --- | CHHPCD > 1.4% HP | CHHPCD > 3.0% HP** | CHHPCD > or = A456-II
1.4% HP | OxivirTB > 1.4% HP | 1.4% HP > or = 0.5% HP | CHHPCD > 1.4% HP | --- | 3.0% HP > or = 1.4% HP | A456-II > or = 1.4% HP
3.0% HP | OxivirTB > 3.0% HP** | 3.0% HP > or = 0.5% HP | CHHPCD > 3.0% HP** | 3.0% HP > or = 1.4% HP | --- | A456-II > or = 3.0% HP
A456-II | OxivirTB > or = A456-II | A456-II > or = 0.5% HP | CHHPCD > or = A456-II | A456-II > or = 1.4% HP | A456-II > or = 3.0% HP | ---
*Mean log10 reductions, standard deviations and 95% confidence intervals were calculated based on replicate measurements (2-4) for inter-product comparisons. Definitions: CHHPCD, Clorox Healthcare™ Hydrogen Peroxide Cleaner Disinfectant; “>” non-overlapping 95% CI (i.e., means were statistically significant at p<0.05); “=” overlapping 95% CI (i.e., means p>0.05). EPA registration claim for: A456-II is 10 minutes; CHHPCD is 30 seconds-1 minute (bactericidal); OxivirTB is 1 minute (bactericidal); and standard HP had no EPA registration.
**Except for against MDR-A. baumannii (103 CFU, contact 1 minute, no FCS)

## Slide 18: References
1. Omidbakhsh N, Sattar SA. Broad-spectrum microbicidal activity, toxicologic assessment, and materials compatibility of a new generation of accelerated hydrogen peroxide-based environmental surface disinfectant. Am J Infect Control 2006;34:251-7.
2. Sattar SA, Adegbunrin O, Ramirez J. Combined application of simulated reuse and quantitative carrier test to assess high-level disinfection: Experiments with an accelerated hydrogen peroxide-based formulation. Am J Infect Control 2002;30:449- 57.
3. Omidbakhsh N. A new peroxide-based flexible endoscope-compatible high-level disinfectant. Am J Infect Control 2006;34:571-7.
4. Omidbakhsh N KN. An accelerated hydrogen peroxide (AHP)-based fast-acting and reusable microbicide for manual disinfection of heat sensitive semi-critical medical devices. Canad J Infection Control 2008;Spring:81-8.
5. Rochon M SN. Products based on accelerated and stabilized hydrogen peroxide: Evidence for cleaning and sanitizing efficiency, environmental and human safety and non-corrosiveness. Canad J Infection Control 1999;Summer:51-5.

## Slide 19: References - continued
6. Springthorpe SV, Sattar SA. Quantitative carrier tests (QCT) to assess the germicidal activities of chemicals: Rationales and procedures. Ottawa: Centre for Research on Environmental Microbiology; 2003.
7. Otter JA, Yezli S, French GL. The role played by contaminated surfaces in the transmission of nosocomial pathogens. Infect Control Hosp Epidemiol 2011;32:687-99.
8. Weber DJ, Rutala WA, Miller MB, Huslage K, Sickbert-Bennett E. Role of hospital surfaces in the transmission of emerging health care-associated pathogens: Norovirus, Clostridium difficile, and Acinetobacter species. Am J Infect Control 2010;38:S25-33.
9. Rutala WA, Weber DJ, Healthcare Infection Control Practices Advisory Committee. Guideline for disinfection and sterilization in healthcare facilities, 2008. In: 'cdcgov/ncidod/dhqp/pdf/guidelines/Disinfection_Nov_2008pdf